Main board model :IPC-I33TB2LE-1C V3.00 (a string of boards)

Verify that the current BIOS is up to date:
Press Delete to enter the BIOS SETUP screen. The latest BIOS screen is as follows:

As shown in red, if the date is 07/14/2021, you do not need to update it

* Otherwise, update the latest BIOS

The brush steps are as follows

Note: Do not cut off the power or restart the computer during the refresh process, otherwise the refresh will fail

1. Make DOS disk (FAT32 format), note: use USB disk
2. Copy all files in the attachment to your USB flash drive note: The files must be placed in the root directory of the USB flash drive

After startup, press F11 to enter the boot device menu and select U disk mode to enter the DOS interface, as shown in the picture

- Enter 1 and press Enter to update the BIOS

- The refresh is complete only when the FPT Operation Passed character is displayed. After the refresh is complete, the system returns to the DOS prompt, as shown in the figure

- After the refresh, restart the computer and press DEL to enter the BIOS during the self-check

- Confirm the UPDATE date and version of the BIOS. Note: The information must be consistent with the picture

6. Select Advanced-------- CPU Configuration-------- TCC Activation offset Note: The value must be consistent with the picture information

- Press F9 to Load Optimal Defaults and select YES

- Press F10. If Save Configuration and Reset is displayed, select YES